## Slide 1
Power-to-Methanol:
Green methanol as an energy carrier and chemical building block
Hans Gelten
HAN H2 EVENT, Arnhem, 2026-01-30

## Slide 2: Green methanol as an energy carrier and chemical building block
Professional Doctorate project
Techno-Economic Analysis: a dynamic and integrated energy/process challenge
Development of the lab-scale methanol set-up

## Slide 3
Power-to-Methanol:
Professional Doctorate project

## Slide 4: Investing energy in hydrogen – accelerating applications of decentralised hydrogen
Part of a Professional Doctorate project (PhD position at Universities of Applied Science), running from feb 2024 – feb 2028
The Professional Doctorate project deals with the complex challenges and strategic goals related to energy, sustainability, and circularity, focusing on the transition towards green energy and the role of hydrogen in addressing these challenges.
Part of the research group Sustainable Energy Systems (professor Richard van Leeuwen)

## Slide 5: Value chain of hydrogen – Sustainable Methanol production

## Slide 6
Power-to-Methanol:
Techno-Economic Analysis: a dynamic and integrated energy/process challenge

## Slide 7: Dynamic and optimized TEA – background (1)
The involved Power-to-MeOH processes:
  CO2 hydrogenation to MeOH
  Dry methane reforming of biogas to syngas and converted to MeOH
  Biomethane decomposition to hydrogen, followed with CO2 hydrogenation
The Techno-Economic Analysis (TEA) is carried out following the methodology of Turton.
ASPEN Plus software is used for (static) simulation of processes

## Slide 8: Dynamic and optimized TEA – background (2)
OptiPlant is used to build and operate an integrated energy-chemical system at minimum cost (developed at DTU in Denmark).
This approach results in:
  A static TEA to compare processes – intermittency or energy prices are neglected
  Optimized TEA integrating energy, processes, intermittency and economics

## Slide 9: Results static & dynamic TEA – levelised cost of MeOH
Benchmark: Fossil based MeOH 530 €/ton
Central e-MeOH 1,080 €/ton
Processes: MeOH from CCU 2,186 €/ton
MeOH from DMR 2,372 €/ton
MeOH from MD 1,865 €/ton
Optimized with Optiplant: MeOH from CCU 1,501 €/ton
MeOH from DMR 2,004 €/ton
MeOH from MD 1,890 €/ton

## Slide 10
Power-to-Methanol:
Development of the lab-scale methanol set-up

## Slide 11: Reason and starting point
The performance of a Methanol reactor can be predicted using simulation software like Comsol.
COMSOL is a general-purpose simulation software package used for modeling and simulating designs, devices, and processes across various fields of engineering and science.

## Slide 13: Reason and starting point
Research carried out by Vera Keijzer (BSc. graduation, Feb-Jul 2025).
A labscale process can be used as validation tool for Comsol.
Starting point is the Methanol set-up developed at HAN University of Applied Science.

## Slide 14: Methanol set-up at HAN

## Slide 15: Development @ Saxion University of Applied Science
Adjustments to the set-up:
  Single pass process
  Continuous process
  Adapted for high pressure
  Equiped with pressure vessel

## Slide 16: Pressure vessel (in cooperation with Boessenkool)

## Slide 17: The set-up
Process Flow Diagram:
  Temperature to 200 C
  Pressure to 50 bar
  Stoichiometric gas mixture (CO2/H2)
  Gas and liquid product/reactants
Research carried out by Ivo Jeeninga
(BSc. graduation, Sep-Jan 2026).

## Slide 18: Catalyst characterization
Catalyst material (Cu/ZnO-Al2O3) is used from HAN
SEM-EDX is used for characterization of pellets

## Slide 19: Current status
Construction of framework, set-up and sensors
Start of leaktesting and test experiments
Ongoing research from Feb – Jul 2026 (Jonathan Wolters (internship) and Mart Oelering)

## Slide 20: Thank you for your kind attention!
More information:
Hans Gelten
j.a.p.gelten@saxion.nl / 0610823289